## Slide 1: Recitation 1
Welcome to Comp Arch!

## Slide 2: About Recitation
Routine:
  10 ~ 20 min of presentation
  Work on practice questions
  Go over answers in the end
Grading
  Showing up
  Participation
  Submit a txt file with the correct name (recitationN.txt)
  Check out at the end

## Slide 3: Linux Environment
You need a Linux environment for your homeworks / projects
Options:
  Anubis LMS: Anubis LMS (anubis-lms.io) (recommended)
  Vital: Gives a remote desktop
  VMware fusion / workstation
  WSL: Windows only
  Linux: Just run linux on your computer
  Mac: Not advised
For any environment other than Anubis, you are responsible for configuring the environment to have all necessary tools

## Slide 4: Number System
Decimal: 1, 2, 5, 10, 20, 50, 100
Binary: 1, 10, 101, 1010, 10100, 110010, 1100100
Hex: 1, 2, 5, A, 14, 32, 64
Binary should have a 0b prefix
Hex should have a 0x prefix or h suffix
Binary -> Hex:
  Break bits into sets of 4
  0011_0010 (50) -> 32
  0110_0100 (100) -> 64

## Slide 5: NOT & AND Gates

## Slide 6: OR & XOR Gates

## Slide 7: NAND Gates

## Slide 8: Algebraic Notation
01-intro-and-gates.pdf page 23

## Slide 9: 2’s Complement
A way to represent negative numbers
Must have fixed bit width
Conversion:
  Flip all bits
  Add 1
  - [00101101 (45)] = 11010010 + 1 = 11010011 (-45)